## Slide 1
FRP base
Assemble condenser coil on base.
EL 538 with Bock Compressor

## Slide 2
Apply SR-998 on base and add 10mm filter matt for evaporator coil.
Assembly :Return air side brackets with revit.
EL 538 with Bock Compressor

## Slide 3
Assembly :Evaporator coil on base.
Evaporator coil insulation using 3mm foam.
EL 538 with Bock Compressor

## Slide 4
Mount vibration absorber plate on compressor mounting plate.
Plate vibration absorber washer on top of vibration absorber Plate.
EL 538 with Bock Compressor

## Slide 5
Mount compressor on vibration Absorber using bolt and nut given with vibration absorber.
Mount compressor accumulator on compressor mounting plate
EL 538 with Bock Compressor

## Slide 6
Mount compressor mounting plate on base.
Assemble txv with check valve assy. and liquid line assy.
EL 538 with Bock Compressor

## Slide 7
Evaporator side brackets Assembly
Insulation liquid line including TXV and bond tape.
EL 538 with Bock Compressor

## Slide 8
Assembly equalizer line for txv.
Compressor Discharge Tube Assembly
EL 538 with Bock Compressor

## Slide 9
Braze revarse valve with discharge C suction from evaporator.
Assemble accumulator with reverse valve assembly.
EL 538 with Bock Compressor

## Slide 10
Assemble condenser in / out line tubes.
Install exhaust fan with plate.
EL 538 with Bock Compressor

## Slide 11
Assemble invertor plate with assembly.
Assemble receiver tank on invertor plate.
EL 538 with Bock Compressor

## Slide 12
AssemblY condenser side equalizer line for txv.
Condenser side TXV bulb mount on discharge line and insulate with 3mm foam.
EL 538 with Bock Compressor

## Slide 13
Mount condenser fan shrouds.
Add 3mm blower foam and install blower with self taping screw.
EL 538 with Bock Compressor

## Slide 14
Adjustable mounting brackets with self taping screw and add with pv seclent on screw.
Add 20mm return air filter using pvc foam.
EL 538 with Bock Compressor

## Slide 15
Add wiring routings and grommet in holes.
Install lifting hooks using m-12 nut.
EL 538 with Bock Compressor

## Slide 16
−Seal all the gaps between condenser coil and base , cond. Coil and fan shroud using foam and sealant.
−Seal all the gaps in grommets using sealant.
Install 13mm foam under evaporator cover using SR-998.
EL 538 with Bock Compressor

## Slide 17
Add 13mm foam invertor side using SR-998.
Mount evaporator and condenser top cover.
EL 538 with Bock Compressor